## Slide 1
Better Batteries
Driving Sustainable Power Solutions for Smartphones
How silicon-carbon anodes could improve performance while battery supply chains become more responsible.
ENG0018 Computer Laboratory • Conference Presentation

## Slide 2
1. Why current smartphone batteries are a problem
Battery technology has to keep pace with increasingly capable smartphones.
Ethical & environmental
Technical
• Cobalt mining has been linked to child labour, unsafe working conditions and environmental degradation in the DRC.
• Mining can contaminate soil and water and damage local ecosystems.
• Greater transparency and international regulation are needed.
• Capacity fades as lithium-ion cells age.
• Lithium plating, structural instability and SEI growth contribute to degradation.
• More powerful processors, AI features and high-refresh displays increase energy demand.
Sources: Rights Lab, University of Nottingham (2025); The Guardian (2024); Rahman and Alharbi (2024)

## Slide 3
2. Silicon-carbon: improving the anode
Silicon-carbon is an evolution of lithium-ion technology rather than a completely different battery chemistry.
Traditional graphite anode
≈372 mAh g⁻¹
Silicon
≈4,200 mAh g⁻¹
• Stable and well established
• Lower theoretical capacity
• Stores far more lithium
• But expands heavily during charging
Carbon helps buffer silicon’s volume changes → better structural stability and cycle performance.
Sources: Park et al. (2024); Park, Lee and Chae (2024)

## Slide 4
3. From laboratory research to real smartphones
The technology is already moving into consumer devices.
≈850
mAh g⁻¹ demonstrated by Si/C composites
• Research reports improved capacity, rate performance and cycle stability compared with conventional graphite.
• HONOR’s silicon-carbon battery was recognised in TIME’s Best Inventions 2025.
• Higher energy density can support longer battery life and more demanding smartphone features.
Why it matters: more capacity in a similar space could make multi-day battery life and increasingly powerful mobile hardware more practical.
Sources: Park et al. (2024); TIME (2025)

## Slide 5
4. Better batteries need more than better performance
Efficiency, sustainability and ethics have to develop together.
Efficiency
Higher capacity Longer battery life Support for demanding features
Sustainability
Longer device lifespans Less pressure for replacement Lower resource demand
Ethics
Fairer working conditions Responsible sourcing Stronger regulation
Silicon-carbon anodes are a promising step forward — but the future of smartphone batteries depends on combining engineering innovation with responsible supply chains.
Conclusion • Based on the conference paper and cited research